## Slide 1: Describing Complex Products as Configurations using APL Arrays
Notes: Dyalog ´06
Describing Complex Products as Configurations using APL Arrays
Lars Wentzel Mandator Sweden
lars.wentzel@mandor.com
Phone +46 705 45 18 06

## Slide 2: Automotive products are getting more complex
The products become more diversified
New models are introduced all the time
The offer changes quickly
New markets emerge
Electronics and software increases the complexity
Notes: Many products today can be customized to a high degree. Traditionally those sold from business to business are highly customized. Today it is common also for consumer products.
Customization can take place in different ways. You can completely engineer a product to the need of a customer. The other extreme is that the customer can adapt the product himself by reconfiguring e.g. the software.
A special variant of this is the ”build to order” products that are customized at the assembly point. This means that products are configured from already designed modules. Automotive products like cars, truck and buses are typically such products. They are special in that the products are expensive, very mechanically complex, there is a high demand on logistics, they contain a lot of electronics and software, design is design involved and finally the competition is hard.
These products become more and more complex since they become more diversified, there are new models introduced frequntly, what is offered to the customer changes all the time, the products are global and you have to adapt to new markets and finally the use of electronics and software increase.

## Slide 3: Increased complexity
Creates new demands on production and business processes
which in its turn creates new demands how the products are described
Notes: The increased complexity creates new demands on production and business processes.
The product must have a modular design so that it is easy and cost effective to customize it. The production and logistics must be flexible and the adaptation to the customer should occur as late as possible in order to have short delivery times. The transportation and delivery must be direct and fast. The sales and order processes must be closely connected to production and logistics processes.
This requires that the product is adequately described so that the customer can order ”his car” and understand the contents and then get a correct price and delivery promise. This order specification should then go directly to production and distribution without extra handling.

## Slide 4: Demands on the Product Description
High information quality
Verification that it is consistent
Transparency – you must understand
Coherent common information across business
Short lead-times to market
Advanced support e.g. for BtO production
Notes: The major demand is for information quality. The product descriptions are so extensive and so complex that this is a serious problem. It takes a lot of manual resources, errors occur when orders are checked and vehicles become wrongly built.
One special requirement is that the whole offer is consistent and verified. This means that you should not show an offer where combinations are not allowed because of technical restrictions. If the cars has 17” breaks you cannot order 15 or 16” wheels.
The offer should be clear and transparent for customers, sales people and for company staff working with e.g. planning.
The information should be common across business. This is to assure that information must not be manually entered in different systems or that you get long lead-time for e.g. orders that must manually processed.
Since new products are introduced all the time and product changes occur frequently you must assure that you have a short lead-time to market with your product description.
I you have a Built to Order production this is more important that the product description process is smooth, clear and efficient.

## Slide 5: A common situation today
No integrated solutions – only part-solutions
Marketing analysis /planning
Sales configurator
Distribution
Design
Production planning
Production
Dealer-Seller-Web
Notes: A common situation today is that the different system do not work with common product information. This may exist in copies that are not timed and that are interpreted in different ways. There may even exist manual translations between different formats and sets of rules.
I seems that the customer offer is the less integrated part while engineering, production and logistics are more connected out of an early need.

## Slide 6: Mandator C-Group
has over the last two decades worked with configuration tasks both in a scientific way on a general level as in practice with the implementation at Volvo Car Corporation
Notes: I and the C-group (Configuration Group) within Mandator have worked in this area for long time. Most of our experience comes from our major customer Volvo Cars.
We handle the product descriptions as such as well as by using it in applications such as Volume & Capacity Planning and Cost Calculation.

## Slide 7: What is a Configurable Product?
  A product like a car model that can be ordered in an almost unlimited no of different configurations
  The product is described by features (variable values) rather than by physical components.
  The features can be combined but there are lots of – usually technical - restrictions. If you order a navigator your car needs a radio.
Notes: A configurable product is a product that can be ordered in an almost unlimited number of variants out of a large selection of standard components. This means that there is nothing such as a list of products. E.g. it is unlikely that two Volvo cars are exactly the same.
The products are described by using features rather than by physical component. A feature can of course be a thing like an engine or a radio. But it can also be a colour or a design element as well as a function like traction control.
A specific product or an order is described by a list of features. This list can be several hundred for a car or a truck e.g.
Engine 3.0, 6 gear automatic gearbox, Monza al 17” wheels, …
Some features can freely be combined. Other do have technical restriction. If you order a navigator system you must also have a radio. You cannot have a build-in phone in the dashboard together with a cup-holder since they use the same space.

## Slide 8: What is a Product or Configuration Structure?
  A list of features per product class that can be ordered and built
  Packages
  Limitations of what can be combined i.e. restrictions or ”rules”
  Timing points i.e. when something changes.
  And also Bill of Material
Notes: A product structure is the complete set of information to describe the product and what combinations of features that can ordered and built.
There are models or classes of products. Each model can have a certain number of features. These can vary depending on market and version. Some features may be standard and some optional.
To simplify ordering and to give discounts you need packages. A package is a set of features.
You have restrictions that limit you choice. These are typically technically restrictions as mentioned. It can also be different design selections or limitations on certain markets.
You need to have timing point i.e. when changes occur in the offer. A colour is introduced at a certain time. And engine is replaced by another. Etc..
The BOM – Bill Of Material – is of course also a part of the product structure. The parts are attached to the features or combinations of features.

## Slide 9: Configuration Rules as Arrays
  The people that founded the Danish company ”Array Technology” have described
  that all configuration rules can be described as simple combinations tables - arrays
  that by using this you can completely verify that your set of rules is consistent
  that you can minimize the size by detecting dependencies
  that using this method you can get very fast responses
Notes: The Danish company Array Technology was founded by Gert Moeller and Claus Erik Jensen.
The have described the principles for describing configuration rules as connected tables or arrays.
By using this principle you can fully verify your product structure i.e. see that everything is consistent and that all features can be used.
You can also minimize the structure by detecting dependencies.
You can get very fast responses when using this information for sales configuration.
While Array Technology has developed a standard product we have attacked specific areas with customized solutions.

## Slide 10: Nested Arrays
The product structure for a model becomes a nested array
We can reuse existing customer solutions in a flexible way
And transfer complex rules to Nested Arrays
You get a mix of tables and restriction arrays
Demo …
Notes: When we handle a product structure we create a nested array of big and small tables.
The flexible approach means that we also can convert customer specific structures to arrays. For the very complex structure of Volvo Cars we had to develop a very specific translation from rules to arrays. At the same time we tried to keep elements from the original description.
What we get is then a mix of tables and restriction arrays.
In our own solution in c-grid product we don’t need a compilation phase but everything is handled as it is when you type.
I will now demonstrate this to you …

## Slide 11: C-Master
The structure that is created is made available for all needs within the company and also for the customers.
The configurations from C-grid or another source are published in the C-Master.
It is made available as a component to give service to other systems. We call this our Master principle using Service Oriented Architecture – SOA.
Notes: When the product structure has been created it must also be published. Even i a big company only a handful of people are busy updating the information.
The use, however, is extensive and varies a lot. It is used for order validation, sales configuration, planning and forecasting, certification, creation of Bill of Material, product presentation, cost calculation, pricing, capacity handling etc..
The structure should be made available for all need in what we call a C-master. This is actually a server that communicates with other systems, primarily through Web-services.
This is really Service Oriented Architecture – SOA – in practice. By keeping information in one server you avoid duplication of information and system logic. New systems can easily hook up and use existing information. With information in array form you can easily create new services.
Everything becomes more integrated, cheaper and faster.

## Slide 12: C-Master Technology Service Oriented concept – SOA
Load balancing and stable response times
Simple Linux or Windows server.
Server keeping product structures in working memory
Web-services
High performance and flexible analysis.
Broad range of services
Notes: There are some important technology use in C-master.
We load-balance by using several parallel processes. This is especially important since we have many different services from less than .1 s, through complex analysis of 15 s or more as well as batch runs of up to 30 minutes.
Everything runs in an ordinary Windows or Linux server.
The product structures are loaded into memory to give fast response.
We communicate using web-services with SOAP-XML format but also through file communication.
We get a very good performance and can easily communicate on-line with other systems.

## Slide 13: CPAM the C-Master System at Volvo Cars
Started as a limited project to translate engineering data in 2002
The use has dramatically increased.
New systems start using the services all the time
All major systems plan to use CPAM
  Sales configurator
  Public information
  Spare-parts information
  Ordering
  Production scheduling
  …
The system runs in an ordinary Windows server.
Notes: CPAM is a C-master at Volvo Cars.
It started as a limited project in 2002 to perform the difficult task of translating the engineering data.
Since then the use has dramatically increased and new systems start using the services all the time. Within short all major system using product data will use CPAM e.g. the sales configurator, ordering, production scheduling, volume and capacity planning, public information, cost calculation and spare-part information for individual cars.
The system runs in an ordinary Window server.

## Slide 14: C-Master Case Project - Stepwise implementation
Support to dealer ordering systems
Support to sales configuration systems
Support to order scheduling systems
Weight calculation
Technical data
Order explosion
Support to planning systems
Cost calculation
Support for special vehicles
Complex analysis
Base car diagnostics
Rules data feed from engineering system
Analysis
Communication
Presentation
Original scope
Installed now
Being developed
Notes: 2002 The initial project delivered functionality for
Translation of configuration rules from the engineering system
Analysis of the rules
Translation services and communication of transactions to other systems
Presentation of rules in the feature table format
Since the first release further functionality has been added:
Complex analysis of products including a specific feature
Base car diagnostics - Verification of base cars taking technical restrictions into account
Weight calculation
  Order weight check.
  Calculation of fuel consumption.
  On-line transaction oriented check of orders
Cost calculation
  Processing of the BoM with fast services of material explosion for cost calculation for multiple cars.
  Option cost calculation based on cost per part number
Support for special vehicles - Full support for presentation of specially equipped vehicles including order validation.
Technical data
  Handling of technical data (dimensions, weight, performance etc.)
  Presentation of the data and on-line services for public systems.
Order explosion - Migration of multi-order explosion. Will speed up execution and save costs
Planning - Generation of forecast orders from base car volume plans and forecasted option take-rates.
Planned new functionality, not yet released:
Support to dealer ordering and sales configuration systems including
  Generation of market authorisation and rules
  Frequent and automatic feed to ordering and configuration systems.
  Immediate on-line order validation
Support to order scheduling systems including
  Validation of each order.
  On-line order exploition for automatic scheduling.

## Slide 15: System Structure
C-Master*
HTTP
Server*
Translation
Services*
Transaction
Services*
Additional
Restrictions*
Translation*
Planning
Order
Scheduling
Dealer
Ordering
Commercial
Cfg Rules
Planning
Order
Scheduling
Dealer
Ordering
Commercial
Cfg Rules
X
Y
Z
*) Functionality delivered by Mandator
Engineering Product Documentation
Update*
Analysis
Feature Tables*
Notes: Input and Data Entry
  The basic source for the C-Master is the engineering product documentation system. The variant conditions together with the order format codes are translated into the possible combinations of order specifications.
  The additional information; model year, markets, 100% options, packages etc. will be added to C-Master by users in the commercial product authorisation process.
Analysis
  Users of the product data will be able to analyse the C-Master and get a result in a Variant Binder format.
Translation Services
  The translation server will provide the existing applications with product data in files with the format that is used today.
  This enables a step-wise implementation of the C-Master as the single product authorisation master
  Existing application will keep a local database for product authorisation in the first instance.
Transaction Services
  The target is to make C-Master common server for product data to all existing and new applications.
  A transaction server will enable a future solution where each application can disconnect the integrated product authorisation data and connect directly to the C-Master.

## Slide 16: Figures of use at Volvo Cars
400 analysis users
6-7 systems using web-services
One request every 5 seconds
Coming: Several request each second
Heavy batch runs
Complicated analysis
7 model years
9 car models
14000 baseline configurations
2600 features
25000 parts
Notes: Here are some figures of the present use of the system and the information handled. We plan for a much more intense use within the next year.
This system has considerably lowered cost in specific areas as well as shortening the processing time.
More and more services are used on-line compared to what had to be done in batch before.

## Slide 17: Server Setup
Master
Session
Slave
Session
Slave
Session
Slave
Session
System 1
SOAP/XML
TCPIP/APL
TCPIP/APL
TCPIP/APL
Load balance using multiple CPU’s
System 2
System n
SOAP/XML
SOAP/XML
Notes: The C-master server is using one master APL session. Other system – including analysis tools – communicate with this master using web-services with SOAP/XML.
Then a number of slave sessions are also running each having part of the data in working memory. The master and slaves communicate using TCP/IP with APL variable format.
When a request arrives the master select the first free slaves and directs the task to this one. When the slave is ready it answers back to the master who forwards the answer to the requesting system.
This is extremely simple and flexible.

## Slide 18: Server Handling
Structure data is read into memory for each slave – could be > 100 mb
Preferred solution: Using threads that can execute simultaneously using separate CPU’s
Problem with TCP/IP interface when requests arrive very close in time.
Slave
Session
Notes: One problem we have is that each slave has to keep data in its own session. This is not so difficult for us since data if fairly stable and is only updated once a week or once a day.
But if you will work with data that changes more rapidly this does not work. Then we would prefer a solution where we could use one session and one set of data and that different threads could process simultaneously utilizing multiple CPU’s.
Another problem that we have detected is that the TCP/IP solution is not working properly, especially at high traffic. A client may fail to get a connect response from out master server session.

## Slide 19: APL Summery
Describing product configurations with APL nested array is extremely powerful
You can provide new and very flexible functions– like showing derived dependencies and bottom-up analysis
Mass validation of orders is very fast by using patterns.
The APL session is extremely simple to use for (web) services.
The C-grid product is possible because of the grid object
C-grid has successfully been converted to version 11
Notes: Here is a short summery of our experience of using Dyalog APL for describing complex products and publishing this information in C-master server.

## Slide 20: APL Improvements
Threads that can utilize multiple processors in servers
Reliable TCP/IP communication
Better memory handling – free unutilized memory
Speed-ups are always welcome
We would like to monitor functions in objects
Notes: And here are wishes for improvement that would help us.

## Slide 21: The Mandator C-group offer
Notes: And finally a summary of what we can do for our customers.